- TMV -7 – Thermostatic mixing valve (factory set to 85 degrees) for multiple emergency eye wash units or a single emergency shower.  Unit shall include a built-in cold water by-pass, rough bronze finish, solid bimetal thermostat, locking temperature regulator with limit stop factory set for 90 degrees, integral check stops, dial thermometer, and recessed stainless steel cabinet with door and lock (optional surface mounted cabinet G3802).

- Performance:  Unit shall have a flow range of 3-GPM to 44-GPM with a maximum pressure loss of 20-PSI and come with a full 1-year warranty.

- Fixture:  Guardian G3807 and G3802